## Slide 1: Burn-in/Stress Test for Reliability: Reducing burn-in time through high-voltage stress test and Weibull statistical analysis
ECE 7502 Class Discussion
Xinfei Guo
19th March 2015

## Slide 2: Reliability
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.
Infant Mortality - Caused by manufacturing process defects, foreign particles, others
that are not caught at the wafer level. e.g. incorrect soldering time, insufficient solder;
Freak failures - Defects within the assembly. e.g. weak wire bonding, poor die
attachment, and induced defects that work properly but fail in a mild stress scenario.
Steady State - Device operation for the rest of its useful life;
Wearout Stage – Fail from overuse or fatigue.
Notes: The reliability of a semiconductor device is determined by its ability to perform its required functions under the stipulated conditions for a finite period of time.
A typical device’s failure characteristics takes the form of a bathtub curve.
With burnin or stress, manufacturer stresses the devices under conditions that accelerate infant mortality.

## Slide 3: Burn-in vs. Stress Test
Burn-in Test
  Subject chips to high temperature while running production tests;
  Catch infant mortality and freak failures;
  Wafer level burn-in or package level burn-in.
Stress Test
  Over-voltage/Current supply
  Might eliminate need of burn-in
[2] Roy, Rabindra, Kaushik Roy, and Abhijit Chatterjee. "Stress Testing: A Low Cost Alternative for Burn-in." VLSI: Integrated Systems on Silicon. Springer US, 1997. 526-539.
Both don’t damage the good components!
Notes: This paper focuses on package level burn-in

## Slide 4
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test
Pre-burn-in
Burn-in
ATE final testing

## Slide 5: Types of burn-in
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.

## Slide 6: Issues/Challenges
Many hours (80% of the total product testing time!!)
Wearout or damage some good dies;
Expensive (burn-in boards/chambers, limited #)
W. Mann et al. “Introduction to Wafer Level Burn-In”, Southwest Test Workshop.

## Slide 7: Solutions
IDDQ Test – wafer level
High Voltage Stress test [1, 2]
Weibull statistical method [1,3]
Wafer level burn in test
Others
Goal of this paper [1]:
A new test flow that reduces the burn-in testing
time and does not sacrifice IC reliability.

## Slide 8: Weibull Statistical Method
A very flexible life distribution model that can be used to characterize failure distributions in all three phases of the bathtub curve
Changing the life-cycle parameter could stretch the distribution curve
Predict future failures
[4] Xie, Min, Y. Tang, and Thong Ngee Goh. "A modified Weibull extension with bathtub-shaped failure rate function." Reliability Engineering & System Safety 76.3 (2002): 279-285.

## Slide 9: Proposed test flow Stage 1: Determine old burn-in parameter
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.

## Slide 10: Proposed test flow Stage 2: New burn-in parameter
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.
Holding the temperature
acceleration constant

## Slide 11: Determine Breakdown voltage
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.
Finding the initial breakdown
Voltages of KGDs
Characterize the target devices
Verify the reliability of the voltage
levels by testing repeatability
Known Good Dies
1
2
3

## Slide 12: Stage 3: HVST Program
Determine patterns that
Provide maximum fault
Coverage in the shortest
Time possible.
Avoid reliability issues
Need to retest at
nominal voltages to confirm
the failure.
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.

## Slide 13: Stage 4: Plan Burn-in
Multiple intervals
Hot test: high temperature
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.

## Slide 14: Stage 5: Validate HVST
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.
Old testing flow
New testing flow
Validate HVST
Ensure true
failures
9000 chips

## Slide 15: Compare to traditional testing
No additional
fallout after 48-hour
Proof burn-in
The results of
two flows are close
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.

## Slide 16: Stage 6: Apply Weibull Analysis
[1] Zakaria, Mohd Fairuz, et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis."
Design & Test of Computers, IEEE 23.2 (2006): 88-98.
Use experimental results to learn ELFR (early life failure rate) against the burn-in duration

## Slide 17: Summary
A combined solution that reduces the burn-in time while avoiding sacrificing the reliability;
Reduction of 90% of the burn-in duration;
The final goal is to eliminate burn-in for package level testing.

## Slide 18: Wafer level vs. Package level Burn-in

## Slide 19: Paper Map
[1] Zakaria et al. "Reducing burn-in time through high-voltage stress test and Weibull statistical analysis." Design & Test of Computers, IEEE 23.2 (2006): 88-98.
[2] Roy, Rabindra et al. "Stress Testing: A Low Cost Alternative for Burn-in." VLSI: Integrated Systems on Silicon. Springer US, 1997. 526-539.
[3] Sumikawa, Nik et al. "An experiment of burn-in time reduction based on parametric test analysis." Test Conference (ITC), 2012 IEEE International. IEEE, 2012.
[4] Xie, Min et al. "A modified Weibull extension with bathtub-shaped failure rate function." Reliability Engineering & System Safety 76.3 (2002): 279-285.
[5] A. Chakraborty and D.Z. Pan "Controlling NBTI degradation during static burn-in testing", ASP-DAC, pp.597-602, 2011.
[6] Wang, Xiaoxiao, et al. "Fast aging degradation rate prediction during production test." Reliability Physics Symposium, 2014 IEEE International. IEEE, 2014.
[2] Basic concepts of Burn-in and Stress Testing
[1] A combined solution
[4] Weibull Analysis
Reduce Burn-in time
[3] Parametric Analysis
Control Reliability
[5] Control NBTI
[6] Stress test for aging research
Use the concept of
Accelerated test

## Slide 20: Glossary
BI – Burin-in
WLBI – Wafer Level Burn-in
HVST – High Voltage Stress Test
PPM – number of devices allowed to fail per one million parts shipped to the customer
KGUs – known good units
ELFR – Early Life Failure Rate

## Slide 21: Questions
In what other situations, do you need to use burn-in or stress test? How do you apply the notion of accelerated test methodology to your research?
On page 98 Table 4, why are the average yields so high? Can you think about how do they calculate the yields here?
Any suggestions for improvement on effectiveness of burn-in/stress test?
How to separate each failure mechanism during burn-in/stress test? Any good ideas?
How to select “Known Good Die”?
Does this method apply to wafer level burn-in test?